Incentive & Measure Specifications

Commercial Energy Solutions

EasySave Program

Prescriptive Incentives

| RETROFIT LIGHTING |
| --- |
| Indoor Incandescent to Standard LED Lighting | $7.50 to $11 per lamp |
| Outdoor Incandescent to Standard LED Lighting | $7.50 to $11.50 per lamp |
| Indoor Incandescent to LED Reflector Lighting | $7.50 to $13 per lamp |
| Outdoor Incandescent to LED Reflector Lighting | $7.50 to $12 per lamp |
| Indoor T12/T8 Fluorescent Tubes to LED Tubes | $6.50 to $13.50 per lamp |
| Outdoor T12/T8 Fluorescent Tubes to LED Tubes | $6.50 to $13.50 per lamp |
| Indoor HID to LED Fixtures | $105 to $190 per fixture |
| Outdoor HID to LED Fixtures | $90 to $190 per fixture |
| Indoor HID to LED Lamps | $45 to $65 per lamp |
| Outdoor HID to LED Lamps | $45 to $65 per lamp |
| De-lamping T12/T8 | $5 to $9 per lamp |
| HID to Linear Fluorescent Lighting-Exterior Only | $0.06 per kWh saved |
| Exit Signs | $50 per sign |
| Daylighting Controls | $0.06 per kWh saved |
| Occupancy Sensors | $65 to $70 per sensor |

| HVAC |
| --- |
| AC Units | $135 to $550 per unit |
| Heat Pumps | $95 to $395 per unit |
| Economizer | $160 per unit |
| Programmable Thermostats | $130 per thermostat |
| HVAC EMS System | $0.60 to $0.90 per square foot |

| REFRIGERATION |
| --- |
| Strip Curtains | $5.00 per square foot |
| Anti-Sweat Heater Controls (low & medium temp) | $14 per linear foot of case |
| Evaporator Fan Motors (ECM) | $55 to $90 per motor |
| Automatic Door Closer | $70 per closer |
| Vending Machine Controls (Snack Machine) | $85 per controller |
| Vending Machine Controls (Beverage and Reach-in) | $85 per controller |

| OTHER MEASURES |
| --- |
| Variable Speed/Frequency Drives | $80 to $385 per horsepower |
| Shade Screens | $2.00 per square foot |
| Plug-Load Smart Strips | $9 per strip |

* Rebates are capped up to a maximum of 50% of incremental cost on selected measures.

Measure Specifications

All equipment removed under the program must be recycled or disposed of in compliance with local requirements. Documentation of disposal may be requested by program staff. A manufacturer’s specification sheet and invoice may be requested for any installed measure.

Lighting

LED Lighting

LED screw-in lamps must replace incandescent or halogen lamps on a one-for-one basis. Reflector lamps must be R, BR or PAR series. A wattage reduction of 60% is required to obtain a rebate.

Linear LED lamps may replace existing two, three, four or eight-foot T12 or T8 lamps. A wattage reduction of 35% is required to obtain a rebate.

Metal halide and high-pressure sodium fixtures may be retrofitted with appropriate LED lamps or replaced with an appropriate LED fixture. A wattage reduction of 50% is required to obtain a rebate.

All LED lamps, linear tubes or fixtures must be either listed as a qualified product with Design Lights Consortium or ENERGY STAR®certified.

Delamping

Delamping is the permanent removal of existing fluorescent lamps. Unused lamps, lamp holders and ballasts must be permanently removed from the fixture to claim the delamping rebate. This measure is applicable when retrofitting T12 to T8, T5 or LED, or simply delamping a T8 fixture. Simply removing T12s from the fixture does not qualify for a rebate.

HID to Linear Fluorescent Lighting – Exterior Only

This measure consists of replacing existing metal halide (MH) and high-pressure sodium (HPS) fixtures with new fixtures with at least two high output T8 or T5 lamps along with high output electronic ballasts. Recommended combinations for existing MH/HPS fixtures are:

- 150 watts to 249 watts replaced with either 2-lamp 4-foot or 4-lamp 2-foot linear fixtures.

- 250 watts to 399 watts should be replaced with 3-lamp linear fixtures.

- 400 watts to 749 watts should be replaced with 4-lamp T5HO or 6-lamp T8HO linear fixtures.

- 750 watts to 999 watts should be replaced with 6-lamp T5HO or two (2) 6-lamp T8HO linear fixtures.

- 1,000 watts or more should be replaced with two (2) 4-lamp T5HO linear fixtures.

All fixtures must have a reflector with a minimum of 90% reflectivity. The new lamps must have a color rendering index (CRI) of ≥ 80. The electronic ballasts must be high frequency (≥20 kHz), UL listed and warranted against defects for five (5) years. Ballasts must have a power factor (PF) of ≥0.90. Ballasts for 4-foot lamps must have a total harmonic discharge (THD) of ≤20% at full light output. Low pressure sodium (LPS) lamps are not eligible to be replaced under this prescriptive incentive.

Exit Signs

High-efficiency exit signs must replace or retrofit an existing incandescent or CFL exit sign. Electroluminescent and light-emitting diode (LED) exit signs are eligible under this category. Non-electrified and remote exit signs are not eligible. All new exit signs or retrofit exit signs must be UL or ETL listed, have a minimum lifetime of 10 years and have an input wattage ≤ 5 watt. A minimum warranty of five (5) years is required.

Daylighting Controls

Eligible controls shall consist of a photosensor that controls on/off, stepped or continuous dimming ballasts. The on/off controller should turn off artificial lighting when the interior illuminance meets the desired indoor lighting level. The stepped controller generally dims the artificial lighting 50% when the interior illuminance levels reach 50% (example for a 2-step controller) of the desired lighting levels. Continuous or dimming controllers dim artificial lighting proportional to the available ambient light. All types of daylight sensor controls are required to be commissioned to ensure proper sensor calibration and energy savings. Systems that allow on/off overrides are not eligible.

Occupancy Sensors

Only passive infrared and/or ultrasonic detectors are eligible. Wall box and wall-, ceiling- or fixture-mounted sensors must be hard-wired to control interior lighting fixtures.

HVAC

Air-Cooled Air Conditioning and Heat Pumps

New air-cooled air conditioning units or heat pumps between 2 and 5 tons with a Seasonal Energy Efficiency Ratio (SEER) rating of at least 15 are eligible for an incentive. They can be either split systems or single-packaged units. All packaged and split-system cooling equipment must meet Air-Conditioning, Heating and Refrigeration Institute (AHRI) standards (210/240 or 340/360), be UL listed and use a minimum ozone-depleting refrigerant (e.g., HCFC or HFC). Evaporative coolers and water source heat pumps are not eligible.

Economizers

The economizer must be capable of modulating to 95% open. Retrofits and replacement of existing HVAC units are eligible. Replacements of existing economizers are not eligible for rebates unless the existing economizer has been non-functional for more than two (2) years. Rebates are not available for economizers that are required per ASHRAE 90.1-2010.

Programmable Thermostats

Equipment must replace a non-programmable thermostat. Programmable thermostats must be capable of 7-day, 5-2 or 5-1-1 programming. Programmable thermostats installed in hotel and motel guest rooms are not eligible for this rebate. Thermostats for evaporative coolers also are ineligible.

HVAC EMS System

This measure is for installing an energy management system to replace thermostats, pneumatic controls or an existing direct digital control (DDC) system. This measure is paid by the square foot of the area controlled. Please call 866-324-5506 or email ces@tep.com for more details.

Variable Refrigerant Flow (VRF) HVAC Systems

New VRF air conditioning or heat pump systems installed as replacements for existing HVAC units/systems that meet or exceed the qualifying Energy Efficiency Ratio (EER) and Integrated Energy Efficiency Ratio (IEER) are eligible for an incentive. All VRF equipment must have efficiencies that have been determined using the rating method outlined in the Air-Conditioning, Heating and Refrigeration Institute (AHRI) standard 1230-2010, be UL listed and use a minimum ozone-depleting refrigerant (e.g., HCFC or HFC).

REFRIGERATION

Strip Curtains

New strip curtains or clear plastic swinging doors must be installed on doorways of walk-in boxes and refrigerated warehouses. This incentive is not available for display cases or replacing existing strip curtains. Incentive is based on square foot of the opening.

Anti-Sweat Heater Controls

For this measure, devices installed that sense the relative humidity in the air outside of the display case and reduce or turn off the glass door (if applicable) and frame anti-sweat heaters at low-humidity conditions are eligible for incentives. Technologies that can turn off anti-sweat heaters based on sensing condensation (on the inner glass pane) also qualify for incentives.

Evaporator Fan Motors

This measure is applicable to the replacement of an existing standard-efficiency shaded-pole evaporator fan motor in refrigerated display cases or fan coil in walk-ins with an electronically commutated motor (ECM).

Automatic Door Closers 
Automatic door closers must automatically close the main insulated door of an existing walk-in cooler or freezer. The auto-closer must firmly close the door when it is within one inch of full closure. Only new installations are eligible for a rebate.

Vending Machine Controls – Beverage, Reach-in and Snack

The controller must include a passive infrared occupancy sensor to turn off lamps and other vending machine systems when the surrounding area is unoccupied for 15 minutes or longer. The beverage case controls should be installed on refrigerated vending machines which contains only non-perishable bottled and canned beverages. The reach-in cooler controller is for glass-front coolers (typically with sliding or pull-open doors) that contain non-perishable goods. The snack machine controls are for non-refrigerated vending machines. For refrigerated equipment, the control logic should power up the machine at two-hour intervals to maintain product temperature.

OTHER MEASURES

Variable Speed Drives on HVAC Fan and Pump

Variable speed drives (VSDs) installed on HVAC fans or pumps are eligible for an incentive. The rated connected motor horsepower must be <50 hp. The installation of a VSD must accompany the permanent removal or disabling of any flow control devices such as inlet vanes, bypass dampers and throttling valves to quality for incentives. This measure applies only to VSDs installed with an automatic control technology.

This measure does not apply to redundant or backup/standby motors that are expected to operate less than 1,200 hours per year, nor does it apply to variable-pitch fans and forward curve with inlet guide vanes, unless applicants supply proof of kWh savings from logged or measured data. This measure also does not apply to replacement of a multi-speed motor or VSDs included on a new variable speed chiller.

Shade Screens

This measure consists of installing fixed exterior mounted shading screens to windows. This rebate is available only for the retrofit of existing windows with east, south or west exposures. The shade screens must have a shading coefficient of 0.30 or less at 30-degree profile angle. The shading coefficient equals the Solar Heat Gain Coefficient (SHGC) x 1.15. Interior window shades such as blinds, drapes and movable door screens are not eligible.

Plug-Load Smart Strips

New plug-load smart strips can be installed to control electricity-using equipment in offices or cubicles, including lighting, monitors, shared copiers and/or printers. Load-controlled and time-controlled smart strips are eligible for rebates. Load-sensing smart plug strips detect a drop in current when a control device enters low-power mode. Timer smart strips turn equipment on and off at a programmed time. This device should be used on equipment that requires a long warm-up.